## Slide 1: بهينه سازي با نقشة کارنو
Karnaugh Map

## Slide 2: Karnaugh Map
  Method of graphically representing the truth table that helps visualize adjacencies
2-variable
K-map
3-variable
K-map
4-variable
K-map
A
B
0
1
0
1
0
1
2
3
0
1
2
3
6
7
4
5
AB
C
0
1
3
2
4
5
7
6
12
13
15
14
8
9
11
10
A
B
AB
CD
A
00
01
11
10
0
1
00
01
11
10
00
01
11
10
C
B
D

## Slide 3: Karnaugh Map
  One cell (in K-map) = a row (in truth table)
  one cell = a minterm (or a maxterm)
  Multiple-cell areas = product terms (sum terms)
A
B
0
1
0
1
0
1
2
3
0
1
2
3
6
7
4
5
AB
C
0
1
3
2
4
5
7
6
12
13
15
14
8
9
11
10
A
B
AB
CD
A
00
01
11
10
0
1
00
01
11
10
00
01
11
10
C
B
D

## Slide 4: Karnaugh Map
0
1
2
3
6
7
4
5
AB
C
A
B
00
01
11
10
0
1
  f1(A,B,C) = m1 + m2 + m4 + m6
  = A’B’C + A’BC’ + AB’C’ + ABC’
A | B | C |  | f1
0 | 0 | 0 | m0 | 0
0 | 0 | 1 | m1 | 1
0 | 1 | 0 | m2 | 1
0 | 1 | 1 | m3 | 0
1 | 0 | 0 | m4 | 1
1 | 0 | 1 | m5 | 0
1 | 1 | 0 | m6 | 1
1 | 1 | 1 | m7 | 0
1
1
1
1
0
0
0
0

## Slide 5: Karnaugh Map
  Numbering Scheme: 00, 01, 11, 10
  Gray Code - only a single bit changes from code word to next code word.
A
B
0
1
0
1
0
1
2
3
0
1
2
3
6
7
4
5
AB
C
A
B
00
01
11
10
0
1
0
1
3
2
4
5
7
6
12
13
15
14
8
9
11
10
AB
CD
A
00
01
11
10
00
01
11
10
C
B
D

## Slide 6: Two-Variable Map
  Any two adjacent cells: differ by ONLY one variable
    complemented in one cell and uncomplemented in the other.
Example:
  m0 (=A’B’) is adjacent to m1 (=A’B) and m2 (=AB’)
    but NOT m3 (=AB)
A
B
0
1
0
1
0
1
2
3

## Slide 7: Two-Variable Map
Example:
  m5 is djacent to m7
0
1
3
2
4
5
7
6
12
13
15
14
8
9
11
10
AB
CD
A
00
01
11
10
00
01
11
10
C
B
D

## Slide 8: Karnaugh Map
  Adjacencies in the K-Map
Wrap from
  first to last column
  top row to bottom row
000
001
010
01
1
1
10
1
1
1
100
101
00
01
11
10
0
1
AB
C
A
B

## Slide 9: 2-Variable Map -- Example
  f(x1,x2) = x1’x2’+ x1’x2 + x1x2’ = m0 + m1 + m2
  Grouping (ORing) of 1s allows simplification
  What (simpler) function is represented by each dashed rectangle?
    m0 + m1 = x1’x2’+ x1’x2 =
    x1’(x2’+ x2 ) = x1’
    m0 + m2 = x1’x2’+ x1x2’ =
    x2’(x1’+ x1 ) = x2’
  Note: m0 covered twice
x2 | 0 | 1
0 | 1 | 1
1 | 1 | 0
x1
0
2
1
3

## Slide 10: Minimization as SOP using K-map
  Enter 1s in the K-map for each product term in the function
  Group adjacent K-map cells containing 1s to obtain a product with fewer variables.
    Groups must be in power of 2 (2, 4, 8, …)
  Handle “boundary wrap”
  Minimum number of groups
  Maximal groups
  Answer may not be unique

## Slide 11: Minimization as SOP
F = ?
A asserted, unchanged
B varies
Cout = ?
F(A,B,C) = ?
G = ?
B complemented, unchanged
A varies
A
B
A
B
Cin
00
01
11
10
0
1
0
0
0
1
1
1
0
1
AB
C
A
00
01
11
10
0
1
0
0
0
0
1
1
1
1
B

## Slide 12: Minimization as SOP
F = A
A asserted, unchanged
B varies
Cout = AB + BCin + ACin
F(A,B,C) = A
G = B'
B complemented, unchanged
A varies

## Slide 13: More Examples
F(A,B,C) = Sm(0,4,5,7)
F =
F'(A,B,C) = Sm(1,2,3,6)
F' =
F' : simply replace 1's with 0's and vice versa
00
C
AB
01
11
10
1
0
0
1
1
1
0
0
A
B
0
1
00
C
AB
01
11
10
0
1
1
0
0
0
1
1
A
B
0
1

## Slide 14: More Examples
F(A,B,C) = Sm(0,4,5,7)
F = B' C' + A C
F'(A,B,C) = Sm(1,2,3,6)
F' = B C' + A' C
F' simply replaces 1's with 0's and vice versa
Why not group m4 and m5?

## Slide 15: Simplification
If we have the Boolean expression (not the truth table)?
  Enter minterms of the function into the map
  Group terms
Example:
  f(a,b,c) = bc’ + abc + ab’

## Slide 16: Simplification
Example:
  f(a,b,c) = bc’ + abc + ab’
 | 1 | 1 | 1
 |  | 1 | 1
c
ab
 | 1 | 1 | 1
 |  | 1 | 1
00
01
11
10
0
1
00
01
11
10
0
1
c
ab
  Result: f(a,b,c) = bc’+ a

## Slide 17: 4-Variable Map
F(A,B,C,D) = Sm(0,2,3,5,6,7,8,10,11,14,15)
F =
m10
m14
m6
m2
10
m11
m15
m7
m3
11
m9
m13
m5
m1
01
m8
m12
m4
m0
00
10
11
01
00
CD
AB

## Slide 18: Four-variable Map Simplification
  One square represents a minterm of 4 literals.
  A rectangle of 2 adjacent squares represents a product term of 3 literals.
  A rectangle of 4 squares represents a product term of 2 literals.
  A rectangle of 8 squares represents a product term of 1 literal.
  A rectangle of 16 squares produces a function that is equal to logic 1.

## Slide 19: 4-Variable Map
F(A,B,C,D) = Sm(0,2,3,5,6,7,8,10,11,14,15)
  Find the smallest number of the largest possible subcubes that cover the ON-set
AB
00
01
11
10
1
0
0
1
0
1
0
0
1
1
1
1
1
1
1
1
00
01
11
10
C
CD
A
D
B

## Slide 20: 4-Variable Map
F(A,B,C,D) = Sm(0,2,3,5,6,7,8,10,11,14,15)
F = C + A' B D + B' D'
  Find the smallest number of the largest possible subcubes that cover the ON-set

## Slide 21: Simplify for POS
F(A,B,C,D) = Sm(0,2,3,5,6,7,8,10,11,14,15)
For POS:
  Group 0’s
  Write down groups as sum terms
  AND them together
AB
00
01
11
10
1
0
0
1
0
1
0
0
1
1
1
1
1
1
1
1
00
01
11
10
C
CD
A
D
B

## Slide 22: Simplify for POS
K-map Method: Circling Zeros to get product of sums form
F = (B’ + C + D) (A’ + C + D’) (B + C + D’)
F’ = B C’ D’ + A C’ D + B’ C’ D
(F’)’ = (B C’ D’ + A C’ D + B’ C’ D)’
F = (B’ + C + D) (A’ + C + D’) (B + C + D’)
Replace F by F’, 0’s become 1’s and vice versa

## Slide 23: Don’t Cares
F(A,B,C,D) = Sm(1,3,5,7,9) + Sd(6,12,13)
Don't Cares can be treated as 1's or 0's if it is advantageous to do so
In Product of Sums form
AB
00
01
11
10
0
0
X
0
1
1
X
1
1
1
0
0
0
X
0
0
00
01
11
10
C
CD
A
D
B
In Sum of Products form

## Slide 24: Don’t Cares
F(A,B,C,D) = Sm(1,3,5,7,9) + Sd(6,12,13)
F = w/o don't cares
F = w/ don't cares
Don't Cares can be treated as 1's or 0's if it is advantageous to do so
A'D + B' C' D
C' D + A' D
In Product of Sums form
AB
00
01
11
10
0
0
X
0
1
1
X
1
1
1
0
0
0
X
0
0
00
01
11
10
C
CD
A
D
B
: F = D (A' + C')
Same answer as above,
but fewer literals

## Slide 25: Example: Comparator
Design Example: Two Bit Comparator
Block Diagram
and
Truth Table
A 4-Variable K-map
for each of the 3
output functions
F
1
1
0
0
0
0
1
0
0
0
0
1
0
0
0
0
1
F
2
0
1
1
1
0
0
1
1
0
0
0
1
0
0
0
0
F
3
0
0
0
0
1
0
0
0
1
1
0
0
1
1
1
0
D
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
C
0
0
1
1
0
0
1
1
0
0
1
1
0
0
1
1
B
0
1
0
1
A
0
0
1
1
F
1
A
B = C D
F
2
A
B < C D
F
3
A
B > C D
A
B
C
D
N
1
N
2

## Slide 26: Comparator K-Maps
F1 =
F2 =
F3 =
A' B' C' D' + A' B C' D + A B C D + A B' C D'
= (A xnor C) (B xnor D)  much simpler, but not in sum of products form
1’s on K-map diagonals make XOR or XNOR
A' B' D + B' C D + A' C
B C' D' + A C' + A B D'

## Slide 27: Example: Two Bit Adder
Block Diagram
and
Truth Table
A 4-variable K-map
for each of the 3
output functions
Cout

## Slide 28: Adder K-Maps
AB
00
01
11
10
0
0
0
0
0
0
1
0
0
1
1
1
0
0
1
1
00
01
11
10
C
CD
A
D
B
K-map for
X
AB
00
01
11
10
0
0
1
1
0
1
0
1
1
0
1
0
1
1
0
0
00
01
11
10
C
CD
A
D
B
K-map for
Y
AB
00
01
11
10
0
1
1
0
1
0
0
1
1
0
0
1
0
1
1
0
00
01
11
10
C
CD
A
D
B
K-map for
Z

## Slide 29: Adder K-Maps
X = A C + B C D + A B D
Z = B D' + B' D = B xor D
Y = A' B' C + A B' C' + A' B C' D + A' B C D' + A B C' D' + A B C D
= B' (A xor C) + A' B (C xor D) + A B (C xnor D)
= B' (A xor C) + B (A xor C xor D)
gate count
reduced if
XOR available
1's on diagonal suggest XOR!
AB
00
01
11
10
0
0
0
0
0
0
1
0
0
1
1
1
0
0
1
1
00
01
11
10
C
CD
A
D
B
K-map for
X
AB
00
01
11
10
0
0
1
1
0
1
0
1
1
0
1
0
1
1
0
0
00
01
11
10
C
CD
A
D
B
K-map for
Y
AB
00
01
11
10
0
1
1
0
1
0
0
1
1
0
0
1
0
1
1
0
00
01
11
10
C
CD
A
D
B
K-map for
Z

## Slide 30: Implementations of Y
Two alternative
implementations of Y
with and without XOR
Note: XOR typically
requires 4 NAND gates
to implement!

## Slide 31: XOR
xy’ + yx’ = xy’ + yx’ + xx’ + yy’
x(y’+x’) + y(x’+y’)
x.(x.y)’ + y. (x.y)’
((x.(x.y)’)’ . (y. (x.y)’)’)’
تبديل مدارها به فقط Nand: بعداً

## Slide 32: Example: BCD Incrementer

## Slide 33: Example: BCD Incrementer
AB
00
01
11
10
0
0
X
1
0
0
X
0
0
1
X
X
0
0
X
X
00
01
11
10
C
CD
A
D
B
AB
00
01
11
10
1
1
X
1
0
0
X
0
0
0
X
X
1
1
X
X
00
01
11
10
C
CD
A
D
B
Z
AB
00
01
11
10
0
0
X
0
1
1
X
0
0
0
X
X
1
1
X
X
00
01
11
10
C
CD
A
D
B
Y
AB
00
01
11
10
0
1
X
0
0
1
X
0
1
0
X
X
0
1
X
X
00
01
11
10
C
CD
A
D
B
X
W

## Slide 34: Example: BCD Incrementer
W = B C D + A D'
X = B C' + B D' + B' C D
Y = A' C' D + C D'
Z = D'
AB
00
01
11
10
0
0
X
1
0
0
X
0
0
1
X
X
0
0
X
X
00
01
11
10
C
CD
A
D
B
AB
00
01
11
10
1
1
X
1
0
0
X
0
0
0
X
X
1
1
X
X
00
01
11
10
C
CD
A
D
B
Z
AB
00
01
11
10
0
0
X
0
1
1
X
0
0
0
X
X
1
1
X
X
00
01
11
10
C
CD
A
D
B
Y
AB
00
01
11
10
0
1
X
0
0
1
X
0
1
0
X
X
0
1
X
X
00
01
11
10
C
CD
A
D
B
X
W

## Slide 35: Order Dependency
AB
00
01
11
10
0
0
1
0
1
1
1
0
0
1
1
1
0
1
0
0
00
01
11
10
C
CD
A
D
B

## Slide 36: Definition of Terms
Implicant:
  Single element of the ON-set or any group of elements that can be combined together
Prime Implicant (PI) (maximal implicant):
  Implicant that if gets larger (covering twice), covers 0s.
Distinguished 1-cell:
  An input combination that is covered by only one PI.
Essential Prime Implicant (EPI):
  A PI that covers one or more distinguished 1-cells.

## Slide 37: Implicant, PI and EPI
6 Prime Implicants:
A' B' D, B C', A C, A' C' D, A B, B' C D
AB
00
01
11
10
0
1
1
0
1
1
1
0
1
0
1
1
0
0
1
1
00
01
11
10
C
CD
A
D
B

## Slide 38: Implicant, PI and EPI
6 Prime Implicants:
A' B' D, B C', A C, A' C' D, A B, B' C D
Essential
Minimum cover =
First: cover EPIs
Then: minimum number of PIs
= B C' + A C + A' B' D
AB
00
01
11
10
0
1
1
0
1
1
1
0
1
0
1
1
0
0
1
1
00
01
11
10
C
CD
A
D
B

## Slide 39: Implicant, PI and EPI
5 Prime Implicants:
B D, A B C', A C D, A' B C, A' C' D
essential
AB
00
01
11
10
0
0
1
0
1
1
1
0
0
1
1
1
0
1
0
0
00
01
11
10
C
CD
A
D
B
Minimum cover =
First: cover EPIs
Then: minimum number of PIs
= A B C‘ + A C D + A' B C + A' C' D

## Slide 40: More Examples
Prime Implicants:
B D, C D, A C, B' C
essential
= BD + AC + B' C
AB
00
01
11
10
0
0
0
0
0
1
1
0
1
1
1
1
1
0
1
1
00
01
11
10
C
CD
A
D
B

## Slide 41: Example
Primes around
A B C' D
AB
00
01
11
10
X
1
0
1
0
1
1
1
0
X
X
0
0
1
0
1
00
01
11
10
C
CD
A
D
B
Example: f(A,B,C,D) = m(4,5,6,8,9,10,13) + d(0,7,15)
Initial K-map
Primes around
A' B C' D'

## Slide 42: Example: Continued
Primes around
A B' C' D'
AB
00
01
11
10
X
1
0
1
0
1
1
1
0
X
X
0
0
1
0
1
00
01
11
10
C
CD
A
D
B
Essential Primes
with Min Cover
(each element covered once)
AB
00
01
11
10
X
1
0
1
0
1
1
1
0
X
X
0
0
1
0
1
00
01
11
10
C
CD
A
D
B

## Slide 43: 5-Variable K-Map

## Slide 44: 5-Variable K-Map

## Slide 45: 5-Variable K-Map
f(A,B,C,D,E) = Sm(2,5,7,8,10,
13,15,17,19,21,23,24,29 31)
= C E + A B' E + B C' D' E'
+ A' C' D E'
BC
DE
00
01
11
10
00
01
11
10
A=0
BC
DE
00
01
11
10
00
01
11
10
A=1
1
1
1
1
1
1
1
1
1
1
1
1
1
1

## Slide 46: 5-Variable K-Map
f(A,B,C,D,E) = Sm(2,5,7,8,10,
13,15,17,19,21,23,24,29 31)
= C E + A B' E + B C' D' E'
+ A' C' D E'

## Slide 47: 6-Variable K-Map

## Slide 48: 7-Variable K-Map
?

## Slide 49: 8-Variable K-Map
?

## Slide 50: Implementing by Nands only
Nand:
  Universal gate
   Can replace gates by equivalent Nand circuit.
    Large circuit (many gates)
  But

## Slide 51: New Symbols for AND/OR
DeMorgan’s Law:
  (a + b)’ = a’ b’ (a b)’ = a’ + b’
=
=
=
=
  a + b = (a’ b’)’ (a b) = (a’ + b’)’

## Slide 52: New Symbols for NOT
  (a . a)’ = a’
A
A
A
A
_
A
A
  (a + a)’ = a’

## Slide 53: NAND-Only Implementation
  Find Sum-of-Products form.
  Inventers can be added
  Equivalent NAND-only

## Slide 54: Another Example

## Slide 55: NOR-Only Implementation
  Find Product-of-Sums form.
  Inverters can be added
  Equivalent NOR-only

## Slide 56: NAND-Only Implementation
NAND-only:
  Another method:
    Group 0s in K-Map
    Find F’ in SOP form
    Add an inverter at the end.

## Slide 57: NAND-Only Implementation
Multi-Level Circuits
  Convert AND/OR gates to proper NAND gates
    AND  AND-NOT symbol
    OR  NOT-OR symbol
  Bubbles must cancel each other;
  otherwise, insert a NAND inverter.
  Take care of appropriate input literals.

## Slide 58: NAND-Only Implementation
Example:

## Slide 59: NAND-Only Implementation
Another Example:

## Slide 60: NAND-Only Implementation
Be careful about branches:
  Gates with multi-fanouts
A
B
C
D
F
X
(a)

## Slide 61: NAND-Only Implementation
Be careful about branches:
  Gates with multi-fanouts
A
B
C
D
F
X
(a)
A
B
C
D’
F
X’
(b)
(c)
A
B
C
D’
F
X’
X

## Slide 62: NOR-Only Implementation
NOR-Only:
  Use “Duality” for the last several slides.

## Slide 63: Analysis of NAND Circuits
  The functionality of a NAND-only circuit is not clear.
  Must be converted to AND-OR circuit.

## Slide 64: Analysis of NAND Circuits
  The functionality of a NAND-only circuit is not clear.
  Must be converted to AND-OR circuit.

## Slide 65: Analysis of NAND Circuits
Example

## Slide 66: Analysis of NAND/NOR Circuits

## Slide 67: Analysis of NAND/NOR Circuits