## Slide 1: Sequential Circuits

## Slide 2: ياداوري
  آموزش تکنيک هاي طراحي و پياده سازي سيستم هاي پيچيده:
سيستم:
  داراي ورودي ها، خروجي ها و رفتار مشخصي است
    اين رفتار توسط فانکشن هايي تعيين مي شود که ورودي ها را به خروجي ها تبديل (نگاشت) مي کند.
    مثال: گوشي تلفن:
      ورودي ها: کليدها
      خروجي ها: صفحة نمايش و سيگنال هاي ارسالي به مرکز تلفن
      رفتار: شماره گيري و ايجاد ارتباط
    مثال: خودرو:
      ورودي ها: پدال ها، سوييچ، فرمان، ...
      خروجي ها: فرمان پيچش و چرخش چرخ ها، فرمان ترمز، ...
      رفتار: ....
    مثال: تلويزيون:

## Slide 3: Sequential vs. Combinational
Combinational Logic:
  Outputs depend only on current input
    TV channel selector (0-9)
Sequential Logic:
  Outputs depend on
    current input and
    current state of the system (which depends on past input values)
  Need some type of memory to remember the current state
inputs
outputs
system

## Slide 4: Sequential Logic
Sequential Logic circuits
  Remembers past circuit state.
  Outputs from the system are “fed back” as new inputs.
  Storage elements:
    Circuits that are capable of storing binary information
    Memory

## Slide 5: Feedback Loop
Feedback:
  A signal s1 depends on another signal whose value depends on s1
    (perhaps with several intermediate signals).
s1
R
S
Q
Q’

## Slide 6: Base of Memory
  Consider the following circuit:
  It can differentiate between two different states
    because it has only one feedback line that can keep one of two values, 0 or 1.
either 0 or 1
P1 = P2 = 0

## Slide 7: Base of Memory
  It can differentiate between two different states
    because it has only one feedback line that can keep one of two values, 0 or 1.
  A circuit with n feedback lines has 2n potential states
  Memory of our circuit depends on the number of its feedback lines:

## Slide 8: SR latch (NOR version)
S
R
R
S
Q
Q’
Q
hold
0
1
Not allowed
S
0
0
1
1
R
0
1
0
1

## Slide 9: SR latch (NOR version)
S
R
R
S
Q
Q’
Truth Table:
Next State = F(S, R, Current State)
S(t) R(t) Q(t) Q(t+)
0 0 0 0 (hold)
0 0 1 1 (Hold)
0 1 0 0 (reset)
0 1 1 0 (reset)
1 0 0 1 (set)
1 0 1 1 (set)
1 1 0 Not allowed
1 1 1 Not allowed
Q
hold
0
1
Not allowed
S
0
0
1
1
R
0
1
0
1

## Slide 10: SR Latch
Truth Table:
Next State = F(S, R, Current State)
S
R
Q
R-S
Latch
Q+
Derived K-Map:
Characteristic Equation:
Q+ = S + R Q
t
S(t) R(t) Q(t) Q(t+)
0 0 0 0 (hold)
0 0 1 1 (Hold)
0 1 0 0 (reset)
0 1 1 0 (reset)
1 0 0 1 (set)
1 0 1 1 (set)
1 1 0 Not allowed
1 1 1 Not allowed

## Slide 11: R=S=1 ??
Illegal output, because
  When S=R=1, both outputs go to zero.
  If both inputs now go to 0, the state of the SR latch depends on delays.
  Hence, “undefined” state.
    MUST be avoided.

## Slide 12: Timing Diagram
100
R
S
Q
Q’
Reset
Hold
Set
Forbidden
State
Reset
Set
Forbidden
State
Race

## Slide 13: Timing Diagram of SR Latch

## Slide 14: SR Latch State Diagram
  Difficulty in observing R-S Latch in the 1-1 state
  Ambiguously returns to state 0-1 or 1-0
Q Q
Q Q
Q Q
0 1
1 0
0 0
Observed State Diagram

## Slide 15: S’R’ Latch (NAND version)
S’
R’
Q
Q’
0 0
0 1
1 0
1 1
S’ R’ Q Q’
0
1
1
0
1 0 Set
0 0 1
0 1 1
1 0 1
1 1 0
X Y NAND
S
R
R-S
Latch
Q
Q’

## Slide 16: S’R’ Latch (NAND version)
S’
R’
Q
Q’
0 0
0 1
1 0
1 1
S’ R’ Q Q’
1
1
1
0
1 0 Hold
0 0 1
0 1 1
1 0 1
1 1 0
X Y NAND
1 0 Set

## Slide 17: S’R’ Latch (NAND version)
S’
R’
Q
Q’
0 0
0 1
1 0
1 1
S’ R’ Q Q’
1
1
0
1
0 0 1
0 1 1
1 0 1
1 1 0
X Y NAND
0 1 Hold
1 0 Set
0 1 Reset
1 0 Hold

## Slide 18: S’R’ Latch (NAND version)
S’
R’
Q
Q’
0 0
0 1
1 0
1 1
S’ R’ Q Q’
1
0
0
1
0 0 1
0 1 1
1 0 1
1 1 0
X Y NAND
1 0 Hold
1 0 Set
0 1 Reset

## Slide 19: S’R’ Latch (NAND version)
S’
R’
Q
Q’
0 0
0 1
1 0
1 1
S’ R’ Q Q’
0
0
1
1
0 0 1
0 1 1
1 0 1
1 1 0
X Y NAND
0 1 Hold
1 0 Set
0 1 Reset
1 0 Hold
1 1 Disallowed

## Slide 20: SR Latch with Control (Enable)
S’
R’
Q
Q’
S
R
C
S R C S’ R’ Q Q’
0 0 1 1 1 Q0 Q0’ Hold
0 1 1 1 0 0 1 Reset
1 0 1 0 1 1 0 Set
1 1 1 0 0 1 1 Disallowed
X X 0 1 1 Q0 Q0’ Hold

## Slide 21: D Latch
  S-R latches are useful in control applications,
    Set a flag in response to some condition
    Reset it when conditions change
  We often need latches simply to store bits presented on a signal line
   D latch
  Can eliminate the undesirable indeterminate state in the RS latch:
    ensure that inputs S and R are never 1 simultaneously.
D
C
D
Latch
Q
Q’

## Slide 22: D Latch (cont.)
D
S R C Q Q’
0 0 1 Q0 Q0’ Store
0 1 1 0 1 Reset
1 0 1 1 0 Set
1 1 1 1 1 Disallowed
X X 0 Q0 Q0’ Store
0 1 0 1
1 1 1 0
X 0 Q0 Q0’
D C Q Q’
S’
R’
Q
Q’
S
R
C

## Slide 23: D Latch Timing Diagram
D
C
D
Latch
Q
Q’
C

## Slide 24: D-Latch Circuit
C D Q | Q+
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 0 1 0 1 0 0 1 1
D
C
D
Latch
Q
Q’
C D
Q+ = C’.Q + C.D

## Slide 25
D Latch with Transmission Gates
C=1  TG1 closes and TG2 opens  Q’=D’ and Q=D
C=0  TG1 opens and TG2 closes  Hold Q and Q’
2
1

## Slide 26: JK Latch
J, K both one yields toggle
Characteristic Equation:
Q+ = Q K’ + Q’ J
K
J
Q
Q’
J-K Latch
J(t) K(t) Q(t) Q(t+)
0 0 0 0
0 0 1 1
0 1 0 0
0 1 1 0
1 0 0 1
1 0 1 1
1 1 0 1
1 1 1 0
Derived K-Map:
K
JK
00
01
11
10
0
0
1
1
1
0
0
1
0
1
Q
(
t
)
J
(hold)
(hold)
(reset)
(reset)
(set)
(set)
(toggle)
(toggle)

## Slide 27: JK Latch Using SR Latch
How to eliminate the forbidden state in SR?
Idea: use output feedback to
guarantee that R and S are
never both one
J, K both one yields toggle
Characteristic Equation:
Q+ = Q K + Q J
J(t) | K(t) | Q(t) | Q(t+)
0 0 | 0 0 | 0 1 | 0 HOLD 1
0 0 | 1 1 | 0 1 | 0 RESET 0
1 1 | 0 0 | 0 1 | 1 SET 1
1 1 | 1 1 | 0 1 | 1 TOGGLE 0
R-S
latch
J
K
R
S
Q’
Q
Q
Q’

## Slide 28: JK Latch Race Condition
Set
Reset
Toggle
Toggle Correctness: Single State changes
Solution: Master/Slave Flipflop

## Slide 29: JK Latch Race Condition
Set
Reset
Toggle
Toggle Correctness: Single State changes
Solution: Master/Slave Flipflop

## Slide 30: Flip-Flops
  Latches are “transparent” (= any change on the inputs is seen at the outputs immediately).
  This causes synchronization problems!
  Solution: use latches to create flip-flops that can respond (update) ONLY at SPECIFIC times (instead of ANY time).

## Slide 31: Alternatives in FF choice
Types of FF
  RS
  D
  JK
  T

## Slide 32: D-FF
0 0 0 1 1 0 1 1 | 0 0 1 1
Truth table
Timing for D Flip-Flop (Falling-Edge Trigger)

## Slide 33: Symbols

## Slide 34: Compare 3 Types

## Slide 35: Rising Edge D-FF
What About Falling-Edge Circuit?

## Slide 36: Setup & Hold Time and Propagation Delay
Setup time:
  D input must be stable for a certain amount of time before the active edge of clock cycle
Hold time:
  D input must be stable for a certain amount of time after the active edge of the clock
Propagation Delay (Clock-to-Output):
  from the time the clock changes to the time the output changes
Propagation Delay (Data-to-Output):
  from the time the data changes to the time the output changes

## Slide 37: Setup & Hold Time and Propagation Delay
Setup and Hold Times for an Edge-Triggered D Flip-Flop
tpLH may be different from tpHL
tp clock-to-output vs. tp D-to-output

## Slide 38: Timing Parameters of a D-Latch

## Slide 39: Edge-Triggered D Flip-Flop
Determination of Minimum Clock Period
Assume:
tco= 5 ns
tp,inv = 2 ns
tsu= 3 ns

## Slide 40: Edge-Triggered D Flip-Flop
Determination of Minimum Clock Period
Assume:
tco= 5 ns
tp,inv = 2 ns
tsu= 3 ns
TCLK = 9
TCLK = 15
TCLK = ?

## Slide 41: Master-Slave FF Configuration Using SR Latches
Enables edge-triggered behavior

## Slide 42
S R CLK Q Q’
0 0 1 Q0 Q0’ Store
0 1 1 0 1 Reset
1 0 1 1 0 Set
1 1 1 1 1 Disallowed
X X 0 Q0 Q0’ Store
Master-Slave FF configuration using SR latches (cont.)
When C=1, master is enabled and stores new data, slave stores old data.
When C=0, master’s state passes to enabled slave (Q=Y), master not sensitive to new data (disabled).
Master
Slave

## Slide 43
Master-Slave J-K Flip-Flop

## Slide 44
Master-Slave J-K Flip-Flop
Sample inputs while clock high
Sample inputs while clock low
Correct Toggle
Operation
P
P’
Master
outputs
Slave
outputs
Set
Reset
T
oggle
1's
Catch
100
J
K
C
P
P‘
‘
Q
Q’

## Slide 45: Edge-Triggered FF
Negative Edge-Triggered
D flipflop
4-5 gate delays
setup, hold times
necessary to successfully
latch the input

## Slide 46: T Flip-Flop
T Flip-Flop
0 0 0 1 1 0 1 1 | 0 1 1 0
Timing Diagram for T Flip-Flop (Falling-Edge Trigger)

## Slide 47: Implementation of T-FF
Implementation of T Flip-Flop

## Slide 48: FFs with Additional Inputs
D Flip-Flop with Clock Enable
The MUX output :
The characteristic equation :

## Slide 49: Asynchronous Preset/Clear
  Many times it is desirable to asynchronously (i.e., independent of the clock) set or reset FFs.
  Example: At power-up, we can start from a known state.
  Asynchronous set == direct set == Preset
  Asynchronous reset == direct reset == Clear
  There may be “synchronous” preset and clear.
D
C
S
R
Q
Q’

## Slide 50: Asynchronous Set/Reset
S
C1
1J
1K
R
IEEE standard graphical symbol for JK-FF with direct set & reset
Cn indicates that Cn controls all other inputs whose label starts with n.
In this case, C1 controls 1J and 1K.
S | R | C1 | 1J | 1K | Q(t+1)
0 | 1 | X | X | X | 1 – Preset
1 | 0 | X | X | X | 0 – Clear
0 | 0 | X | X | X | Undefined
1 | 1 |  | 0 | 0 | Q(t) – Hold
1 | 1 |  | 0 | 1 | 0 – Reset
1 | 1 |  | 1 | 0 | 1 – Set
1 | 1 |  | 1 | 1 | Q(t)’ -- Complement
Function Table

## Slide 51: Asynchronous Inputs
  Asynchronous Clear
  Asynchronous Preset

## Slide 52: Synchronous Reset